## Slide 1: Transcranial dirct current stimulation (tdcs)
Humanise Workshop:
Transcranial direct current stimulation
(tdcs)
HUMANISE CORE FACILITY
HUMAN AND ARTIFICIAL MINDS AND BODIES

## Slide 2: Transcranial direct current stimulation (tdcs)
What is it?
  Non-invasive brain stimulation technique used in psychology, neuroscience and clinical research
  Weak direct current over the surface of the scalp via electrodes
  Modulates cortical excitability and can influence brain function
  Can be used in research on cognition, behaviour, neurorehabilitation
What is it?

## Slide 3: Transcranial direct current stimulation (tdcs)
How does it work?
  Delivers weak direct current (typically 1-2 mA) through electrodes placed on the scalp
  The electrical current flows from a positive electrode (anode) to a negative electrode (cathode)
How does it work?

## Slide 4: Transcranial direct current stimulation (tdcs)
Mechanism of action
  tDCS is believed to modulate neuronal membrane potentials  neuronal excitability
  Effects depend on stimulation parameters, electrode placement, brain state etc.
Mechanism of action

## Slide 5: Transcranial direct current stimulation (tdcs)
Anodal vs. cathodal tdcs
  ANODAL
  Anode (positive electrode) is placed over the target brain region
  Typically associated with increased cortical excitability
  Neurons are more likely to fire
  CATHODAL
  Cathode (negative electrode) is placed over the target brain region
  Typically associated with decreased cortical excitability
  Neurons less likely to fire
Anoval VS. Cathodal tDCS

## Slide 6: Transcranial direct current stimulation (tdcs)
Advantages and disadvantages
  Advantages
  Non-invasive (safe)
  Inexpensive
  Portable and easy to use
  Can be combined with behavioural tasks or trainings
  Can be combined with imaging techniques (fMRI, EEG)
  Applications in cognitive enhancement and neurorehabilitation
  Disadvantages
  Spatial resolution is relatively low (compared to other NIMBS techniques)
  Current distribution in the brain is diffuse and difficult to control precisesly
  High variability across participants
  Results across studies are diverse/difficult to replicate between studies
  60-70% of the current does not reach deeper structures
Asvantages and disadvantages

## Slide 7: Transcranial direct current stimulation (tdcs)
Techni cal and practical considerations
  Physiological factors that may affect tDCS results: skull thickness, cerebrospinal fluid (CSF), grey matter, white matter  different electrical conductivities
  Cortical gyri and sulci affect how electric fields interact with neurons
  Lateralization in different brain regions: e.g., the cortex = contralateral organization; cerebellum = ipsilateral organization
  Duration? Typically 10-30 minutes
  Timing? Concurrent stimulation (at the same time as the task) vs. Before the task?  depends on the nature of the task and your research question
  Placement?  electrodes can be placed on the head (cephalic placement) or on the head an arm/upper body/chin
Technical and practical considerations

## Slide 8: Transcranial direct current stimulation (tdcs)
Safety considerations
  Informed consent
  Participant monitoring at all times! Ramp-up + ramp-down of current are the most salient changes to the participant
  Inclusion/exclusion criteria  NO metal implants in the head, history of epilepsy/seizures, damaged scalp at the site of electrodes
  Poor contact = can increase risk of burns

## Slide 9: Transcranial direct current stimulation (tdcs)
How to generate codes

## Slide 10: Transcranial direct current stimulation (tdcs)
How to generate codes step-by-step
PRESS POWER BUTTON
PRESS ANY KEY TO CONTINUE
PRESS 2 (ADMINISTRATION)
ENTER PIN, THEN PRESS “#” (IF YOU WOULD LIKE TO USE THIS DEVICE, WE WILL PROVIDE PIN TO YOU)
PRESS 3 (STIM PROFILES)
CHOOSE A TRANSPARENT PROFILE (= IS NOT IN USE)
ENTER AN INTENSITY
ENTER RAMP DURATION
ENTER DURATION
PRESS “1”: ANODAL STIMULATION
PRESS “2”: SHAM STIMULATION
PRESS 1 (DC)
ENTER THE NUMBER OF CODES YOU NEED

## Slide 11: High-Definition Transcranial direct current stimulation
comparison field simulation of 4x1 HD vs bilateral
Example: Right-dlPFC

## Slide 12
Our aim:
Facilitate research collaboration by providing access to labs and use of research equipment at the VUB for empirical research
Fee waiver
Users who do not have sufficient financial resources to pay the requested fees may request a fee waiver to use our facilities and equipment for a limited number of years
Condition: users will add this fee to their budget proposal(s) in their next grant proposal(s).

## Slide 13
We warmly encourage you to get in contact with us for potential collaboration opportunities!
You can find us via
Our website: https://humanise.research.vub.be/en
Email: humanize@vub.be
Please check out our current offer for equipment and facilities here: https://humanise.research.vub.be/en/equipment

## Slide 14: References and literature on tdcs methodology
Bastani, A., & Jaberzadeh, S. (2013). A-tDCS differential modulation of corticospinal excitability: The effects of electrode size. Brain Stimulation, 6(6), 932–937. https://doi.org/10.1016/J.BRS.2013.04.005
Bikson, M., Datta, A., & Elwassif, M. (2009). Establishing safety limits for transcranial direct current stimulation. Clinical Neurophysiology : Official Journal of the International Federation of Clinical Neurophysiology, 120(6), 1033. https://doi.org/10.1016/J.CLINPH.2009.03.018
Brunoni, A. R., Nitsche, M. A., Bolognini, N., Bikson, M., Wagner, T., Merabet, L., Edwards, D. J., Valero-Cabre, A., Rotenberg, A., Pascual-Leone, A., Ferrucci, R., Priori, A., Boggio, P. S., & Fregni, F. (2012). Clinical Research with Transcranial Direct Current Stimulation (tDCS): Challenges and Future Directions. Brain Stimulation, 5(3), 175. https://doi.org/10.1016/J.BRS.2011.03.002
Esmaeilpour, Z., Shereen, A. D., Ghobadi-Azbari, P., Datta, A., Woods, A. J., Ironside, M., O’Shea, J., Kirk, U., Bikson, M., & Ekhtiari, H. (2020). Methodology for tDCS integration with fMRI. Human Brain Mapping, 41(7), 1950–1967. https://doi.org/10.1002/HBM.24908
Ferrucci, R., Cortese, F., & Priori, A. (2015). Cerebellar tDCS: How to Do It. Cerebellum, 14(1), 27–30. https://doi.org/10.1007/s12311-014-0599-7
Grimaldi, G., Argyropoulos, G. P., Bastian, A., Cortes, M., Davis, N. J., Edwards, D. J., Ferrucci, R., Fregni, F., Galea, J. M., Hamada, M., Manto, M., Miall, R. C., Morales-Quezada, L., Pope, P. A., Priori, A., Rothwell, J., Tomlinson, S. P., & Celnik, P. (2016). Cerebellar Transcranial Direct Current Stimulation (ctDCS): A Novel Approach to Understanding Cerebellar Function in Health and Disease. Neuroscientist, 22(1), 83–97. https://doi.org/10.1177/1073858414559409
Krause, B., & Kadosh, R. C. (2014). Not all brains are created equal: The relevance of individual differences in responsiveness to transcranial electrical stimulation. In Frontiers in Systems Neuroscience (Vol. 8, p. 25). Frontiers. https://doi.org/10.3389/fnsys.2014.00025
Krause, B., Márquez-Ruiz, J., & Cohen Kadosh, R. (2013). The effect of transcranial direct current stimulation: a role for cortical excitation/inhibition balance? Frontiers in Human Neuroscience, 7(SEP). https://doi.org/10.3389/FNHUM.2013.00602
Li, L. M., Uehara, K., & Hanakawa, T. (2015). The contribution of interindividual factors to variability of response in transcranial direct current stimulation studies. Frontiers in Cellular Neuroscience, 9(MAY), 181. https://doi.org/10.3389/FNCEL.2015.00181/BIBTEX

## Slide 15: References and literature on tdcs methodology
Nardo, D., Creasey, M., Negus, C., Pappa, K., Reid, A., Josephs, O., Callaghan, M. F., & Crinion, J. T. (2021). Transcranial direct current stimulation with functional magnetic resonance imaging: a detailed validation and operational guide. Wellcome Open Research, 6, 143. https://doi.org/10.12688/wellcomeopenres.16679.1
Nasseri, P., Nitsche, M. A., & Ekhtiari, H. (2015). A framework for categorizing electrode montages in transcranial direct current stimulation. Frontiers in Human Neuroscience, 9(FEB), 54. https://doi.org/10.3389/FNHUM.2015.00054/BIBTEX
Sadeghihassanabadi, F., Misselhorn, J., Gerloff, C., & Zittel, S. (2022). Optimizing the montage for cerebellar transcranial alternating current stimulation (tACS): a combined computational and experimental study. Journal of Neural Engineering, 19(2), 026060. https://doi.org/10.1088/1741-2552/AC676F
Stagg, C. J., & Nitsche, M. A. (2011). Physiological basis of transcranial direct current stimulation. In Neuroscientist (Vol. 17, Issue 1, pp. 37–53). https://doi.org/10.1177/1073858410386614
Thair, H., Holloway, A. L., Newport, R., & Smith, A. D. (2017). Transcranial direct current stimulation (tDCS): A Beginner’s guide for design and implementation. Frontiers in Neuroscience, 11(NOV), 1–13. https://doi.org/10.3389/fnins.2017.00641
van Dun, K., Bodranghien, F. C. A. A., Mariën, P., & Manto, M. U. (2016). TDCS of the cerebellum: Where do we stand in 2016? Technical issues and critical review of the literature. Frontiers in Human Neuroscience, 10(MAY2016), 199. https://doi.org/10.3389/FNHUM.2016.00199/BIBTEX
Woods, A. J., Antal, A., Bikson, M., Boggio, P. S., Brunoni, A. R., Celnik, P., Cohen, L. G., Fregni, F., Herrmann, C. S., Kappenman, E. S., Knotkova, H., Liebetanz, D., Miniussi, C., Miranda, P. C., Paulus, W., Priori, A., Reato, D., Stagg, C., Wenderoth, N., & Nitsche, M. A. (2016). A technical guide to tDCS, and related non-invasive brain stimulation tools. Clinical Neurophysiology, 127(2), 1031–1048. https://doi.org/10.1016/J.CLINPH.2015.11.012
Wörsching, J., Padberg, F., Goerigk, S., Heinz, I., Bauer, C., Plewnia, C., Hasan, A., Ertl-Wagner, B., & Keeser, D. (2018). Testing assumptions on prefrontal transcranial direct current stimulation: Comparison of electrode montages using multimodal fMRI. Brain Stimulation, 11(5), 998–1007. https://doi.org/10.1016/j.brs.2018.05.001